## Slide 1
B
C
D
E
F
Point A (for “application”)
marks the point when the vacuum is applied
A
Point B (for ‘beginning’) is the onset of the steady state period and continues until point C. This period corresponds to the linear decrease of the ice cylinder height which maintains intimate contact with the glass wall, and without changing the shape of the ice interface.
Point C (for “curvature”) is the when the ice starts to preferentially dry down the sides of the glass wall. The perimeter of the ice interface changes from planar to a curved surface and ultimately resembles a dome
At Point D (for “dome”) there is no ice cylinder in contact with the glass wall and only an ice dome covers the base of the vial
Point E (for “end”) is the end of ice sublimation, i.e., the point in time when the last trace of ice disappears
Point F (for “finish”) marks the finish of the primary drying stage
The period from D to E is called the recovery phase and results from the reduction in the projected area of the ice mass, covering the surface of the vial.
A reduction of this area progressively reduces the capacitive losses to ground, allowing the capacitance between the electrodes to be recovered
The “ABC ..” of TVIS observations on the changing shape of the ice mass
Shrinkage of the ice dome across the base of the vial
The period from A to D is called the reduction phase and results from the decrease in the height of the ice cylinder. Ice has a dielectric constant of between 110 – 140 (depending on its temperature) and its presence between the electrodes increases the capacitance of the electrode assembly; any decrease in height therefore decreases the measured capacitance
Reduction in the height of the ice mass in the space bounded by the electrodes
Source : GS-(2024_01_20)